## Slide 1: Simulating Lyu (2018) Experiment
Also simulated by Jeff Silva (Arclight Research Consulting)
Used Hydrus unsaturated flow and transport model

## Slide 2: Model configuration and infiltration rate
Lyu’s experiment
One dimensional
15 cm long, inner diameter 2cm (Lyu et al, 2018, pg4)
Porosity = 0.33 (saturated water content)
Pore Velocity measured: 37 cm/hr
Darcy velocity 8.32 cm/hr (??) = 37 * 0.33 = 12.21 cm/hr
Experiments was also conducted at pore velocities of 17, 69, and 137cm/hr
Pore volume: 24.3 cm3 (??) 0.33 * pi * 1^2 * 15 = 15.55 cm3 when saturated.
So for recharge rate of 12.21 cm/hr, volumetric rate is 12.21 * pi * 1^2 = 38.36 cm3/hr So 1 PV for this case is 15.55/38.36 hr = 0.405 hours = 1 pore volume
See spreadsheet for PVs of other saturations
  BUT: PVs used in graphs are for saturated conditions of 1 PV = 0.405 hours
PFOS concentration : 0.01, 0.1, 1 mg/L (lyu pg3)
Vadose Zone
Water table
15 cm
Q = 12.21 cm/hr
h = 0

## Slide 3
Lyu et al, 2018, Table 1.

## Slide 4: Soil parameters (Silva, pg 5)
Soil moisture content = 0.28 (VG parameter, alpha=0.008cm-1, n=3.2) – Silva pg6
Silva pg6
Sr = theta_r / theta_s = 0.078/0.33 = 0.2364
Lyu, 2018
Gives S = 1 very much above the water table. Will need to give a very low boundary head to make S = 0.68 or 0.86.
Using SWR = 0.22, alpha = 12.6 [cm-1]; beta = 1.16; Brookn = 4
Gives SW = 0.681 (at equilibrium) with bottom head = -1.8 cm
Diffusion coefficient = 5.4e-06 cm2/s = 0.01944 cm2/hr

## Slide 5: A-W Adsorption Parameters
Area computed as: Aaw = (1-Sw)Amax
  Amax is 216 cm2/cm3
  Also on Lyu pg 6
PFOA AWI adsorption coefficient (kaw)
In this case, Kaw looks independent from solute concentration because initial concentration is at 1mg/L
10-2.4 = 0.004 = Kaw for PFOA BUT text gives different values depending on concentration
PFOA AWI adsorption coefficient (kai)
Lyu pg7
Lyu pg7
Lyu pg8
Silva pg7

## Slide 6: For different source concentrations
Chart: 
Saturatred curves match. Unsaturated ones do not match with or without dispersion / diffusion

## Slide 7: Different Saturations
Saturatred curves match. Unsaturated ones do not match with or without dispersion / diffusion (too much adsorption on a-w.
Expt. 0.68 curve looks too close to full saturation one (compared to with no Kd) showing that a-w partitioning is less than soil-water
Chart: 
Figure 2 of Lyu (2018)

## Slide 8: For different source concentrations saturated PVs
No dispersion/diffusion
Chart: 

## Slide 9: For different source concentrations saturated PVs
With dispersion/diffusion
Chart: 

## Slide 10: Different Saturations Saturated PVs
Chart: